## Slide 1
Flex-E Rex Soldering Kit
Find more classes and trainings at our website!
https://schulich.libguides.com/m2z
5. Insert the second LED from the backside while aligning the flat part on the LED with the line on the PCB. Try to pull the LED as close to the board as possible by wiggling the LED and pushing into the board. Try to keep the LED centered and trim the wires after.
6. Insert coin cell and check that both LEDs work with the switch. If the LEDs do not work, check that the battery isn’t upside down or that the LEDs aren’t soldered backwards! The flat spot on the LED should be on the same side as the flat line on the PCB.
7. Place the assembled PCB into the Flex-E Rex body while aligning the PCB holes with posts and then attach the second half of the head.
Finished!
Flex-E Rex Soldering Kit
Find more classes and trainings at our website!
https://schulich.libguides.com/m2z
5. Insert the second LED from the backside while aligning the flat part on the LED with the line on the PCB. Try to pull the LED as close to the board as possible by wiggling the LED and pushing into the board. Try to keep the LED centered and trim the wires after.
6. Insert coin cell and check that both LEDs work with the switch. If the LEDs do not work, check that the battery isn’t upside down or that the LEDs aren’t soldered backwards! The flat spot on the LED should be on the same side as the flat line on the PCB.
7. Place the assembled PCB into the Flex-E Rex body while aligning the PCB holes with posts and then attach the second half of the head.
Finished!

## Slide 2
Parts List
2x LEDs
1x Switch
1x PCB
2x Resistors
1x Battery Holder
1x Coin Cell
1x Flex-E Rex Head Half
1x Flex-E Rex Body and Head
Assembly Steps
1. Place the switch and battery holder as shown and solder into place from the backside. For a good solder joint apply heat to both the pad and component for 1-3 seconds and then press solder into the heated area. See the image below for tips!
0. Pre-heat soldering iron to ~350*C/~650*F
!!Note the orientation of the battery holder!!
2. Place and solder the resistors as shown. Make sure to trim the leads after soldering!
4. Place and solder the first LED against the spacer as shown. Align the line on the PCB and the flat part of the LED for correct polarity. Try to center the LED and trim excess wire when done.
3. Locate the LED spacer in the bag or still attached to the inside of the Flex E Rex head half and insert into the PCB eye hole as shown.
Parts List
2x LEDs
1x Switch
1x PCB
2x Resistors
1x Battery Holder
1x Coin Cell
1x Flex-E Rex Head Half
1x Flex-E Rex Body and Head
Assembly Steps
1. Place the switch and battery holder as shown and solder into place from the backside. For a good solder joint apply heat to both the pad and component for 1-3 seconds and then press solder into the heated area. See the image below for tips!
0. Pre-heat soldering iron to ~350*C/~650*F
!!Note the orientation of the battery holder!!
2. Place and solder the resistors as shown. Make sure to trim the leads after soldering!
4. Place and solder the first LED against the spacer as shown. Align the line on the PCB and the flat part of the LED for correct polarity. Try to center the LED and trim excess wire when done.
3. Locate the LED spacer in the bag or still attached to the inside of the Flex E Rex head half and insert into the PCB eye hole as shown.